## Slide 1: Robot Teknolojisine Giriş Yrd. Doç. Dr. Erkan Uslu, Doç. Dr. Sırma Yavuz, Doç. Dr. Fatih Amasyalı, Ar. Grv. Nihal Altuntaş, Ar. Grv. Furkan Çakmak D011 Cuma 14:00-17:00 03

## Slide 2: Robotic Arm
Link : Individual rigid bodies that make up the robot
Joint : Contacts connecting two links
Manipulator : Main body of the robot = links + joint + oth. stuctural elmnts.
Wrist : Joints, links between forearm and end effector
End-Effector : Part mounted on the last link
Actuators : Drivers that modify geometric location/position of joints
Sensors : Elements that detect and collect info. about internal, external states
Controller : Collects sensor info., plan geometric motion, control comm. between robot and its environment

## Slide 3: Robotic Arm : Joint types
Active – Passive
  Active : Controlled by actuator
    Revolute – Prismatic
  Passive :
    Revolute – Prismatic – Cylindrical – Screw – Spherical - Planar

## Slide 4: Robot Classification - Geometry
Open-loop (serial) robot : kinematic structure doesn’t make a loop chain
Closed-loop (parallel) robot : kinematic structure makes a loop chain
Hybrid robot = serial + parallel

## Slide 5: Robot Classification - Geometry
Open looped robots are classified according to their first 3 joints starting from the base  total of 72 configurations
Link1
Link2
Link3
Base
Joint1
Joint2
Joint3
Revolute (R) or Prismatic (P)
Revolute or Prismatic
Revolute or Prismatic
Parallel () or
Orthogonal () or
Perpendicular ()
Parallel or
Orthogonal or
Perpendicular

## Slide 6: Robot Classification - Geometry
Parallel link (): If adjacent joint axes on a link are parallel
Orthogonal link (): If adjacent joint axes on a link intersect at 90°
Perpendicular link (): If adjacent joint axes on a link are at 90° with respect to their common normal

## Slide 7: Robot Classification - Geometry
(Selective compliance assembly robot arm - SCARA)
(Articulated)
(Spherical)
(Cylindrical)
(Cartesian)

## Slide 8: Robot Classification –Degree of Freedom-DoF
The number of joints of a manipulator  DoF
Typical manipulator has 6 DoF : 3 DoF for positioning, 3 DoF for orientation
Manipulator with more than 6 DoF  redundant manipulator

## Slide 9: Robot Classification – Workspace
Workspace  total volume of space that the end-effector can reach
Rechable workspace  volume of space where each point can be reached at least in one orientation
Dexterous workspace  volume of space where each point can be reached in all possible orientations

## Slide 10: Robot Classification – Workspace
Cartesian | SCARA | Articulated | Parallel

## Slide 11: Robot Classification – Actuation
Electric, hydrolic, pneumatic, magnetic,...
Robot Classification – Control
Open-loop control
Closed-loop control : Point-to-point control, Continuous path control
Robot Classification – Application
machine loading, pick and place, welding, painting, assembling, inspecting, sampling, manufacturing, biomedical, assisting, remote controlled mobile, telerobot, ...

## Slide 12: Preliminary for Forward Kinematics

## Slide 13: Rotation Kinematics – Rotation About Global Coordinates – Rotation About Z-axis – Vector Math
G: Global frame, B: Rigid body frame,
: unit vectors in B, : unit vectors in G

## Slide 14: Rotation Kinematics – Rotation About Global Coordinates – Rotation About Z-axis– Vector Math

## Slide 15: Rotation Kinematics – Rotation About Global Coordinates– Vector Math
The calculation of local frame (1) orientation relative to global frame (0) can be achieved by projecting unit vectors in local frame onto global frame unit vectors

## Slide 16: Rotation Kinematics – Rotation About Global Coordinates – Rotation About Z-axis– Geometric

## Slide 17: Rotation Kinematics – Rotation About Global Coordinates – Rotation About Y-axis

## Slide 18: Rotation Kinematics – Rotation About Global Coordinates – Rotation About X-axis

## Slide 19: Rotation Kinematics – Rotation About Global Coordinates – Successive Rotations
Find the final position of P(5,30,10), after; 30 deg rotation about Z-axis, followed by 30 deg rotation about X-axis and 90 deg rotation about Y-axis.

## Slide 20: Rotation Kinematics – Rotation About Global Coordinates – Global rot., local pos.
If the global coordinate of a point after 60 deg rotation about Z-axis is (4,3,2), find the coordinates of this point in its local frame
?

## Slide 21: Rotation Kinematics – Rotation About Global Coordinates – Global rot., local pos.
If the global coordinate of a point after 60 deg rotation about Z-axis is (4,3,2), find the coordinates of this point in its local frame

## Slide 22: Rotation Kinematics – Rotation About Local Coordinates
Defining the position of a point located in the global frame with respect to a local frame:
If global frame and local frame
has a relative rotation among
local axes:

## Slide 23: Eurler Angles
 | Euler angle I | Eurler Angle II
Sequence of rotations | Rotation about | Rotation about
 | Rotation about | Rotation about
 | Rotation about | Rotation about
 | Euler angle I | Eurler Angle II
Sequence of rotations |  | 

## Slide 24: Global Roll – Pitch – Yaw Angles: (45 deg examples)
Rotation about global X-axis is called roll, rotation about global Y-axis is called pitch and rotation about global Z-axis is called yaw.
The global roll-pitch-yaw rotation matrix is given as

## Slide 25: Local Roll – Pitch – Yaw Angles
Rotation about local x-axis is called roll/bank, rotation about local y-axis is called pitch/attitude and rotation about local z-axis is called yaw/spin.
The local roll-pitch-yaw rotation matrix is given as

## Slide 26: Local vs. Global Rotation
Global rotation matrix is the inverse of local rotation

## Slide 27: Local vs. Global Rotation
Global rotation matrix is the inverse of local rotation

## Slide 28: General Transformation
There is always a transformation matrix that maps components of a vector from reference frame to reference frame , where and shares a common origin .

## Slide 29: Rotation Matrix Properties

## Slide 30: Homogeneous Transformations – Rigid Motion
Global coordinates () of a point in a rigid body () with freely moving local coordinate frame can be given as:
Where is the displacement between local and global frames, and is the transformation matrix that maps B to G.

## Slide 31: Homogeneous Transformations
Rigid motion can also be written with a homogeneous transformation matrix as:

## Slide 32: Homogeneous Transformations
Translation only homogeneous transform : Axes of B and G are parallel
Rotation only homogeneous transform : Origins of B and G are coincident

## Slide 33: Homogeneous Transformations
Find the global coordinates of a point in a rigid body which started coincident with global frame origin then rotated 45 deg about X-axis and then tranlated to (3,5,7):
Global coordinates of a point in the rigid body with the defined motion is:

## Slide 34: Homogeneous Transformations
The most general form of homogeneous transformation matrix

## Slide 35: Forward Kinematics

## Slide 36: Forward Kinematics
The coordinates of a point relative to the base frame () can be calculated by the combined transformation matrix () of a link robot arm and the point’s coorinates at the final frame ()

## Slide 37: Forward Kinematics - R∥R∥R Robot

## Slide 38: Forward Kinematics - R∥R∥R Robot

## Slide 39: Forward Kinematics - R∥R∥R Robot

## Slide 40: Forward Kinematics - R∥R∥R Robot

## Slide 41: Forward Kinematics - R∥R∥R Robot
Position of the tip of the robot relative to the base is:

## Slide 42: Forward Kinematics - R∥R∥R Robot
At rest position:

## Slide 43: Forward Kinematics - R∥P⊢P Robot

## Slide 44: Forward Kinematics - R∥P⊢P Robot

## Slide 45: Forward Kinematics - R∥P⊢P Robot

## Slide 46: Forward Kinematics - R∥P⊢P Robot

## Slide 47: Forward Kinematics - R∥R∥P SCARA and wrist

## Slide 48: Forward Kinematics - R∥R∥P SCARA and wrist
y3
x3
y4
x4

## Slide 49: Forward Kinematics - R∥R∥P SCARA and wrist

## Slide 50: Forward Kinematics - R∥R∥P SCARA and wrist
x1
y1
y2
x2
a2

## Slide 51: Forward Kinematics - R∥R∥P SCARA and wrist

## Slide 52: Inverse Kinematics

## Slide 53: Inverse Kinematics
Inverse kinematics : determination of joint parameters for a given set of kinematic chain, transformation matrices and desired end-effector position/orientation.
Inverse kinematics:
  Closed form solutions
    Geometric
    Algebric
  Numerical Methods

## Slide 54: Inverse Kinematics - R⊢P
Given that determine and

## Slide 55: Inverse Kinematics - R∥R
Given that determine
There may be two, one or no solution to the problem

## Slide 56: Inverse Kinematics - R∥R
Law of cosines:

## Slide 57: Inverse Kinematics - R∥R
Law of sines: