## Slide 1: Robot Teknolojisine Giriş Yrd. Doç. Dr. Erkan Uslu, Doç. Dr. Sırma Yavuz, Doç. Dr. Fatih Amasyalı, Ar. Grv. Nihal Altuntaş, Ar. Grv. Furkan Çakmak 05

## Slide 2: Dead (deduced) Reckoning
Estimating the entire trajectory of a moving robot
Dead-reckoning systems are based on estimating position relative to sensors. These sensors can be accelerometers, gyroscopes, wheel encoders, infrared sensors, cameras etc.
Odometry is a sub topic of dead-reckoning and based on wheel displacement calculations

## Slide 3: Dead (deduced) Reckoning
Kinematic Model
  Open loop motion model, position update with given linear/angular velocity
Wheel Odometry
  Position update by wheel encoders
Laser Scan Matcher
  Position update with matching consecutive laser scans
Visual Odometry
  Position update with matching consecutive images
Inertial Odometry
  Position update with motion (accelerometer), rotation (gyroscope) and heading (magnetometer) sensors
Combined Odometry
  Position update with combined sources of odometries and sensors

## Slide 4: Odometry Errors
bump
ideal case
different wheel diameters
carpet
and many more …

## Slide 5: Kinematic Model (Velocity Model)

## Slide 6: Kinematic Model (Velocity Model)

## Slide 7: Kinematic Model (Velocity Model)

## Slide 8: Wheel Odometry
Odometry is obtained integrating sensor reading from wheel encoders
Pose estimation is carried out similar to kinematic model, except that distances traveled by the wheels are calculated from sensor reading

## Slide 9: Wheel Odometry
If a robot starts from a position , and the right and left wheels move respective distances and , what is the resulting new position ?

## Slide 10: Wheel Odometry
Let’s model the change in angle and distance travelled by the robot

## Slide 11: Wheel Odometry

## Slide 12: Wheel Odometry
Average orientation is

## Slide 13: Laser Scan Matcher
Scan-matching tries to incrementally align two scans or a map to a scan, without revising the past/map
Types
  Iterative Closest Point
  Scan-to-scan
  Scan-to-map
  Map-to-map
  Feature based

## Slide 14: Laser Scan Matcher
ICP (iterative closest point) : verilen noktalar kümesinden referans yüzeyine hangi roto-translasyon (dönüş ve öteleme ) ile ulaşılabileceğini yinelemeli olarak hesaplayan bir yöntemdir
noktalar kümesi için roto-translasyon
ile dönüştürülmüş noktalar kümesinin ’te Öklid izdüşüm karşılıkları olan noktalar ile olan uzaklıklarını üzerinden en küçüklemeye çalışmaktadır

## Slide 15: Laser Scan Matcher
ICP için en küçüklenecek kısıt denklemi
ile üzerine Öklid izdüşüm
ilk dönüşüm durumundan hareketle ICP için yinelemeli kısıt denklemi

## Slide 16: Visual Odometry
A camera (or an array of cameras) rigidly attached to a robot
Construct a 6-DOF trajectory using the video stream coming from this camera(s)
Using just one camera  Monocular Visual Odometry
Using two (or more) cameras  Stereo Visual Odometry
In monocular VO, trajectory estimation can be given in scale factor
In stereo VO, exact trajectory estimation can be carried out (in meters)
If (distance to objects)/(stereo distance) >>  degenerates to monocular VO

## Slide 17: Visual Odometry – Stereo VO - Algorithm
Input :
  ,
  ,
  ,
Output :

## Slide 18: Visual Odometry – Stereo VO - Rectification
Two cameras are used
Intrinsic callibration (lens distortion, imaging plane orienteation)
Extrinsic callibration (position & orientation of two cameras with respect to a global frame)

## Slide 19: Visual Odometry – Stereo VO – Disparity Map

## Slide 20: Visual Odometry – Stereo VO – Feature Detection
Features from accelerated segment test (FAST)
A corner point has either of the following at 16 neighborhood circle
  Set of N contiguous pixels that are brighter than (center + threshold)
  Set of N contiguous pixels that are darker than (center – threshold)

## Slide 21: Inertial Odometry
Using data provided by the inertial measurement unit (IMU) to continuously infer the relative change in position, velocity and orientation with respect to a starting point
Gyroscope  data on angular velocity
Accelerometer  data of linear acceleration (g included)

## Slide 22: Inertial Odometry - Pitfalls
Integration drift : Small errors in the measurements of acceleration and angular velocity cause progressively larger errors in velocity—and even greater errors in position
Gravity : The dominating component in the accelerometer data is gravity, even slight errors in orientation make the gravity ‘leak’ into the estimates
The sequential nature of the problem makes the errors accumulate

## Slide 23: Modeling Uncertainty in Motion
If and with and error terms,
produces errors in the direction of motion
results in , (supposed to be =1, =0)
Modelling and with a probability distribution one can estimate the pose of the robot probabilistically

## Slide 24: Modeling Uncertainty in Motion

## Slide 25: Preliminary for Kalman F. and Extended K.F.

## Slide 26: Gauss (Normal) Distribution
-
-+
Gauss distribution can be described by where
  is the mean and
  is the standart deviation, is called variance

## Slide 27: Estimating a Value
Suppose there is constant value (distance to wall)
Two different sensors measure this value
First one observes with variance
Second one observes with variance
Can we merge these evidences?

## Slide 28: Estimating a Value

## Slide 29: Multivariate Gauss Distribution
Multivariate (d-variable) Gauss distribution can be described by where
  is the mean vector and
  is the covariance matrix

## Slide 30: Expectations
For a random variable the expected value is
Expected value of a vector is by component
For uniform distribution

## Slide 31: Variance and Covariance
Variance of a random variable is
Covarince matrix is
For uniform distribution

## Slide 32: Independent Variation
Generate 100 samples duples for x and y Gaussian random variables with and

## Slide 33: Dependent Variation
c and d are random variables generated by c=x+y and d=x-y

## Slide 34: Kalman Filter

## Slide 35: Stocastic Models of Uncertain World
Actions u are uncertain
Observations are uncertain
The state x is unobservable
The sense vector z provides noisy information about x

## Slide 36: Kalman Filter
Kalman filter estimates
Kalman filter requires the following
  Next state probability is a linear function of its arguments with additive noise
  Measurement probability must be linear in its argumnets with additive noise
  Initial belief of must be normal distribution

## Slide 38: Kalman Filter
Prediction (ACT) based on previous estimate and odometry
Observation (SEE) with on-board sensors
Measurement Prediction based on prediction and map
Matching of observation and map
Estimation position update

## Slide 39: Kalman Filter – ACT – using motion model and its uncertainities

## Slide 40: Kalman Filter – SEE – estimation of position based on perception and map

## Slide 41: EKF
The assumptions of linear state transitions and linear measurements with added Gaussian noise are rarely fulfilled in practice
For example, a robot that moves with constant translational and rotational velocity typically moves on a circular trajectory, which cannot be described by linear next state transitions
Extended Kalman filter (EKF) overcomes the linearity assumption

## Slide 42: EKF
The next state probability and the measurement probabilities are governed by nonlinear functions g and h
The extended Kalman filter (EKF) calculates an approximation to the true belief by Linearization via Taylor Expansion

## Slide 43
Non-Linear transformation of Gaussian variable
EKF approximation

## Slide 44: Combined Odometry
Estimete robot pose based on partial pose measurements from different sources
robot_pose_ekf ROS package uses Extended Kalman filter with 6D model to combine measurements from wheel odometry, IMU sensor and visual odometry

## Slide 45: RPE – Laser Scan Matcher - No IMU

## Slide 46: RPE – Laser Scan Matcher + IMU