## Slide 1: Robot Teknolojisine Giriş Yrd. Doç. Dr. Erkan Uslu, Doç. Dr. Sırma Yavuz, Doç. Dr. Fatih Amasyalı, Ar. Grv. Nihal Altuntaş, Ar. Grv. Furkan Çakmak 06

## Slide 2: Localization
The robot determines its position in the environment  localization
If one can attach an accurate positioning sensor (For instance a GPS that gives exact position, works indoor/outdoor) to a mobile robot  there would be no such problem as localization
Sensor accuracy is not suffecient, some sensor doesn’t work outdoors, some doesn’t work indoors
Concern can be on global position or relative position

## Slide 3: Localization – Odometric Model
Deterministic error sources: (can be eliminated by proper calibration)
  Limited resolution (time increment, measurement resolution...)
  Misalignment of wheels
  Unequal wheel diameter
  Wheel contact point variation
  Unequal floor contact (slipping, nonplanar surface...)
Non-deterministic error sources :
  Range error
  Turn error
  Drift error
Over time {turn error, drift error} >> {range error}

## Slide 4: Localization – Odometric Error Model
Odometric position updates can give only a very rough estimate of the actual position
Owing to integration errors of the uncertainties of and the motion errors during the incremental motion , the position error based on odometry integration grows with time

## Slide 5: Localization – Odometric Error Model
, =+

## Slide 6: Localization – Odometric Error Model
We want to give a probabilistic estimation for new position and covariance matrix
Assume that initial covariance at starting point is known and is
Assume that motion increment covarinace is given as
In it is also assumed that errors for individual wheels are independent
Variances of wheel errors are propotional to distance traveled, and depend on the robot and the environment (calculate experimentally)

## Slide 7: Localization – Odometric Error Model

## Slide 8: Localization – Odometric Error Model – Preliminary

## Slide 9: Expected Value and Variance of Linear Functions of Independent Random Variables

## Slide 10: Taylor Series Expansion of a Infinitely Differentiable Function at

## Slide 11: Taylor Series Expansion of a Infinitely Differentiable Two Variable Function at

## Slide 12: Error propagation: Combining uncertain measurements
is an input signal with known probability distribution
What can be said about the probability distribution of ?
: covarience matrix for outputs
: covarience matrix for inputs
: Jacobian matrix

## Slide 13: Robot Localization Problem
Robot starts from a precisely known location
Robot is moving in a known environment
Robot can track its motion using odometry (proprioceptive sensor)
Due to odometry uncertainity, robot will become very uncertain about its position
To keep position uncertainity from growing unbounded, robot must localize itself in relation to the map
To localize robot might use its exteroceptive sensors (map+sensor)
Odometry and map+sensor can be combined for localization

## Slide 14: Robot Localization Problem
Two step update : prediction (odometry) + perception (map+sensor)
Prediction contributes uncertainity to robots belief
Perception refines belief
Why not only use perception?  Perception optimization would take too long
Probabilistic map-based localization methods:
  Markov Localization
  Kalman Filter Localization

## Slide 15: Robot Localization Problem
Probabilistic map-based localization methods - PDF
  Markov Localization
    Robot’s belief state can be represented by any arbitrary probability density function
  Kalman Filter Localization
    Robot’s belief state is represented using a single Gaussian pdf

## Slide 16: Robot Localization Problem
Probabilistic map-based localization methods – pro/con
  Markov Localization
    Starts form any unknown position
    Robot tracks multiple position hypothesis
    Discrete representation of space
    Can recover from any ambiguous situation
  Kalman Filter Localization
    Starts from an initially known position
    Robot can get lost if uncertainity becomes too large
    Continuous world representation

## Slide 17
(a) Prediction phase: the start position is assumed to be known, and therefore the probability density function is a Dirac delta function. As the robot starts moving, its uncertainty grows due to the odometric error, which accumulates over time. (b) Perception phase: the robot uses its exteroceptive sensor (e.g., a rangefinder) to measure the distance from the right wall, and computes the position , which is in conflict with the current position estimated in the action phase. The perception update corrects the new position to and as consequence its uncertainty shrinks

## Slide 18
Joint Probability for independent random variables
Conditional Probability
Conditional Probability for independent variables

## Slide 19
Theorem of total probability: discrete and continuous probability
Bayes Rule:

## Slide 20: Belief Representation
Robot’s belief model regarding its position on the map  Belief Representaion
Single-hypothesis belief : Robot’s belief about position on the map is a single unique point
Multiple-hypothesis belief : The robot tracks not only just a single possible position but a possibly infinite set of positions

## Slide 21: Terminology
: robot location at time
: robot path
: odometry reading at time
: odometry reading sequence
: measurement at time
: sequence of measurements
: 2D coordinates of landmarks
: true map, consists of 2D landmark positions

## Slide 22: Belief Distributions
A robot cannot measure its true pose (state)
Robot estimates its pose based on sensor’s data
The best guess about robot state is called belief
, (perception update)
: belief about robot state before new observation (prediction update)

## Slide 23: Probabilistic Map-Based Localization Terminology
: initial robot location, if initial location is unknown uniform distribution over all poses, if initial location is perfectly known Dirac Delta distribution, if Kalman localization is used Gaussian distribution
: map is assumed to be known
: observation, : control input ; data available
: probabilistic motion model, if and are normally distributed, and can be linearly approximated than can also be given as Gaussian
: probabilistic measurement model

## Slide 24: Classification of Localization Problems
Position tracking : initial location is assumed to be known, position is updated based on previous position
Global localization : initial location may be unknown, localize globally
Kidnapped robot problem : problem defined when robot is kidnapped and moved to another location, same as global localization if robot realizes having been kidnapped, it is difficult to realize being moved

## Slide 25: Markov Localization
Markov localization can use an arbitrary probability density function for robot’s pose belief
This is achieved with discrete number of possibel robot poses
Markov localization addresses global localization, position tracking and kidnapped robot problem
Markov localization = Bayes Filter

## Slide 26: Markov Localization
Markov assumption: position estimation only depends on previous position
Prediction update
Perception update

## Slide 27: Illustration of Markov Localization

## Slide 28: Monte Carlo Localization
Represent belief by a set of discrete weighted samples
: represent location
: importance factor

## Slide 29: Monte Carlo Localization - MCL
Markov localization is the foundation of MCL
MCL uses random weighted samples
Each particel is a potential pose of the robot
Proposal distribution is the motion model of the robot
Observation model is used to compute importance weight
Example MCL

## Slide 30: Kalman Filter Localization
Prediction update: Gaussian error motion model
Measuremement update :
  Observation step
  Measurement prediction
  Matching step
  Estimation step

## Slide 31: Kalman Filter Localization - Prediction update
: the position is estimated by the motion model,
: variance of the estimated position

## Slide 32: Kalman Filter Localization - Measurement Update
: sensor measurement are obtained (measurements are in the sensor/local frame, total of n different single observations)
Sensor measurement error can be modelled as
Using and map measurement prediction is carried out  knowing that robot is at and having map what are the predicted observations
Map features are transformed into local frame observations with

## Slide 33: Kalman Filter Localization - Measurement Update
Two probabilities (prediction and sensor readings)  Calculate the probability that both are true  multiplication
: position estimation is refined by matching
: variance is also refined
: covariance calculated in multiplication of two Gaussians

## Slide 34: Illustration of Kalman Filter Localization

## Slide 35: Landmark-based Localization
Requires significant environmental modification  placement of predefined landmarks
When a landmark is in the field of view of the robot localization is frequent and accurate
Between landmarks robot uses dead-reckoning

## Slide 36: Globally Unique Localization
Robot with camera can use bag of features (local features) and search the dataset for the most similar image
Robot with a laser scanner can use angular histogram and search the dataset for the most similar position

## Slide 37: Positioning Beacon Systems
Requires deploying an active beacon system or retroreflective markers
Given known position of the active/passive beacons one can identify its position

## Slide 38: Route-based Localization
In cases robot moves only within a predefined path, markings on the path (magnetic, reflective,...) enable localization