## Slide 1: Robot Teknolojisine Giriş Yrd. Doç. Dr. Erkan Uslu, Doç. Dr. Sırma Yavuz, Doç. Dr. Fatih Amasyalı, Ar. Grv. Nihal Altuntaş, Ar. Grv. Furkan Çakmak 07

## Slide 2: Path Planning
Given
a START pose,
a desired GOAL pose,
a geometric description of the ROBOT and
a geometric description of the WORLD
find a path that moves the robot gradually from start to goal.

## Slide 3: Configuration Space – Robot Arm
Suppose a robot arm has k degrees of freedom
Every state of the robot arm can be described with k-real values
K-values representing a point in the k dimensional space : configuration space

## Slide 4: Configuration Space – Robot Arm

## Slide 5: Configuration Space – Mobile Robot
Assume robot is simply a point
Each obstacle is inflated by the size of robots radius

## Slide 6: Path Planning
Graph Search
  Graph Construction
    Visibility Graph
    Voronoi Diagram
    Exact Cell Decomposition
    Approximate Cell Decomposition
  Deterministic Graph Search
    Breadth-First Search
    Depth-First Search
    Dijkstra’s Algorithm
    A*
    D*
  Randomized Graph Search
    Rapidly Exploring Random Trees
Potential Field Path Planning

## Slide 7: Visibility Graph
Vertices of the graph are:
  Start
  Goal
  Vertices of the obstacles visible from each other
Visibility graphs are optimal in terms of path length

## Slide 8: Voronoi Digram
Maximize the distance between the robot and the obstacles
Diagram points are equidistant from two or more obstacles

## Slide 9: Exact Cell Decomposition
Cell boundaries are based geometric criticality
In extremely sparse environmets representation is efficient

## Slide 10: Approximate Cell Decomposition
Approximate Cell Decomposition uses cells with the same simple pre defined shape in different scale

## Slide 11: Deterministic Graph Search
Expected total cost :
Path cost :
Edge traversal cost :
Heuristic cost :
Can be defined for a node and an adjacent node

## Slide 12: Deterministic Graph Search
 Depth-First, Breadth-First
AND  Dijkstra’s Algorithm
 Optimal A*
 Suboptimal A*

## Slide 13: Breadth-First Search
Algorithm begins with the start node
Explores all of its neighboring nodes
Then, for each of these nodes, it explores all their unexplored neighbors and so on.
This process goes as, marking a node “active”, exploring each of its neighbors and marking them “open”, and finally marking the parent node “visited
The algorithm proceeds until it reaches the goal node where it terminates.

## Slide 14: Breadth-First Search

## Slide 15: Depth-First Search
Depth-first search expands each node up to the deepest level of the graph
May provide non optimal solutions
May have better space complexity compared to breadth-first search

## Slide 16: Depth-First Search

## Slide 17: Dijkstra’s Algorithm
Similar to breadth-first search
Edge costs may assume any positive value
Guarantees solution optimality
No heuristic is used
Is a greedy algorithm yet produces an optimal solution

## Slide 18: Dijkstra’s Algorithm

## Slide 19: A*
Similar to Dijkstra
Includes an underestimated function of the cost to go
Heuristic function is the distance from any node to goal

## Slide 21: D*
Incremental replanning version of A*
From start to goal A* path is calculated
If a change occures, instead of calculating path from scratch, only effected states are recomputed

## Slide 22: Rapidly Exploring Random Trees
Doesn’t require graph decomposition
Obstacle map is required
RRTs grow a graph online during search
Random nodes are generated and edges are grown from nearest nodes to randomly generated nodes
Solution optimality is not guaranteed
Deterministic completeness is not guaranteed

## Slide 23: Rapidly Exploring Random Trees

## Slide 24: Potential Field Path Planning
Calculates a field/gradient across robot’s map
The goal acts as an attractive force
Obstacles act as repulsive forces
Superposition of repulsive and attractive forces is applied to robot
Smoothly guides robot to goal, simultaneously avoiding obstacles
Gradient of potential field

## Slide 25: Potential Field Path Planning